## Slide 1
HACKATHON
Dynamic Route Optimizer
PS 5 • The Last-Mile Impossible Route
A prototype for continuously adapting delivery routes when real-world conditions change.
Challenge
Routes become outdated within minutes.
Approach
Feasible assignment + dynamic re-planning.
Demo
Breakdown • Traffic • New Priority Order

## Slide 2
1. The Problem
Why static delivery routes are not enough
Traffic changes
A route that was efficient at 9:00 can become inefficient minutes later.
Vehicle breakdown
One unavailable vehicle can invalidate several active deliveries.
New priority order
An urgent order can appear while drivers are already on the road.
PS 5 requires continuous adjustment of routes and vehicle assignments.
The system should consider capacity, delivery windows, driver limits, travel time, and delivery priority.
The goal is dynamic adaptation—not just finding one route once.
PS 5 • Dynamic Route Optimizer • 2

## Slide 3
2. Our Solution
A dispatcher-focused dashboard and route engine
Orders
📦 Evaluate and adapt
Constraints
⚙ Evaluate and adapt
Route Engine
🧠 Evaluate and adapt
Live Event
⚡ Evaluate and adapt
Updated Route
🔄 Evaluate and adapt
Designed for a delivery operator / logistics manager to monitor active routes.
The prototype uses simulated coordinates so the routing logic can be demonstrated without claiming live GPS data.
Affected routes are re-planned when conditions change.
PS 5 • Dynamic Route Optimizer • 3

## Slide 4
3. Routing Logic
Hard constraints first, then route selection
Hard constraints
Vehicle available • enough capacity • delivery window feasible • driver stop limit
Travel factors
Distance and estimated travel time influence assignment.
Priority
High-priority orders receive stronger protection in the scoring.
Assignment Score ≈ distance + travel time + workload + waiting
Lower score = more suitable vehicle, after hard constraints are satisfied.
PS 5 • Dynamic Route Optimizer • 4

## Slide 5
4. Dynamic Event Handling
The main PS 5 demonstration
Normal
Routes active
Vehicle breakdown
Remove unavailable vehicle → reassign affected orders
Traffic change
Update travel time → re-plan affected route
New priority order
Evaluate available vehicles → insert new delivery
PS 5 • Dynamic Route Optimizer • 5

## Slide 6
5. System Architecture
Prototype structure
Frontend
HTML • CSS • JavaScript Dashboard • map • controls
Route Engine
Constraint checks • scoring • assignment • re-planning
Event System
Breakdown • traffic • priority order • reset
Order model: location, package size, priority, delivery window.
Vehicle model: capacity, driver, availability, current location, stop limit.
Outputs: current routes, vehicle status, order assignment, event log.
PS 5 • Dynamic Route Optimizer • 6

## Slide 7
6. Demo Flow
01
Generate Routes
Show normal assignments and estimated travel time
02
Breakdown
V002 fails → affected orders are reassigned
03
Traffic
Congestion near Customer B → affected route is recalculated
04
New Order
High-priority order appears → system assigns a feasible vehicle
PS 5 • Dynamic Route Optimizer • 7

## Slide 8
7. What We Built & Next
Working prototype: route generation, capacity checks, priority, travel time, delivery windows, driver limits.
Dynamic handling: vehicle breakdown, traffic change, new priority order, route/status updates.
Prototype limitation: simulated map coordinates rather than live road/GPS routing.
PS 5 Goal
Continuously adapt routes and vehicle assignments as conditions change.
PS 5 • Dynamic Route Optimizer • 8